## Slide 1: Signal and System Final Project
ECG signal processing
Name: 唐郁翔 ID: 10811040

## Slide 2: TABLE OF CONTENTS Background 01 Method 02 Result 03 Discussion 04

## Slide 3: OUR Goal
透過訊號處理的方式，處理掉心電圖的雜訊(denoise)，和做到基線移除(baseline correction)，並且找出QRS 複合波(QRS complex)，來幫助我們更容易地去判讀心電圖，最後找出ST節段(ST segment)不正常的案例。

## Slide 4: Research Background 01

## Slide 5: What is ST Segment?
ST節段:
表示QRS複合波（QRS complex）至T波之間的間期，一般介於 0.005 至 0.150 秒之間。

## Slide 6: What can we learn form ST Segment?
正常的情況
節段上升(elevation): 表示可能有心肌透壁性梗塞（Transmural myocardial infarction）的狀況。
節段下降(depression): 則可能代表心內膜下梗死、低鉀血症，毛地黃苷中毒（digitalis toxicity）
T反轉(T-inversion):可能表示冠心性缺血（coronary ischemia）、Wellens症候群、左心室肥大（left ventricular hypertrophy），或中樞神經系統疾病。
Notes: Elevation: 心肌梗塞的警訊
Depression:
Inversion:代表心肌缺血

## Slide 7: Research Method 02

## Slide 8: Programming Flowchart
Step 3
Remove Baseline
Step 1
Find Noise Frequency
Step 0
Load data
Step 4
Extract Features
Step 2
Filter Design
& De-noise

## Slide 9: Step 1: Find Noise Observation
發現雜訊出現在50Hz(200Hz)
Using FFT

## Slide 10: step 2: Design Filter
Freq Specification
Fpass1=49
Fstop=49.99
Fstop2=50.04
Fpass2=52
Magnitude Specification
Apass1=0.5
Astop=58
Apass2=1
Basic Setting
Bandstop FIR Filter
Order=822
Window=Kaiser
Filter Designer

## Slide 11: step 3: Remove Baseline
Find Baseline
Remove Baseline
How is Baseline Generated
+baseline'
Respiration,
electrode impedance variations,
body movements.
msbackadj()
Notes: Electrode: 電極

## Slide 12: Step 4: Moving Window Features
Create a filter
Create a moving window integration filter
Setting threshold
Mark QRS
Using for loop:
R: max value
S: min value
Q: min value before R
01
02
03
Notes: 藍色視為分後訊號
紅色是平方後訊號
綠色的是視窗後訊號

## Slide 13: Research Result 03

## Slide 14: Sample no.3 VS. Sample no.4 No. 3 No. 4
T-wave inversion
Normal ST segment

## Slide 15: Signal to Noise Ratio Noise EKG SNR Sample No.3 Filtered Signal SNR 33.01
Sample No.4
11.66
8.06
31.79

## Slide 16: Discussion 04

## Slide 17: Pros & Cons of Finite Impulse Response Advantages Disadvantages
Simple & Stable
Having linear phase response
Good performance
Non-causal
Requires large storage
Harder to implement than IIR
Requires complex computational techniques

## Slide 18: Pros & Cons of Fast Fourier Transform Advantages Disadvantages
Fast, more efficient
low computing complexity, which means it makes the calculation easier.
Frequency limitation: 0~0.5*sample rate(Nyquist point)
Need to apply a window weighting function to compensate for spectral leakage
Notes: FFT的範圍最多到0.5倍的sample rate(Nyquist point/frequency)，因此大於奈奎斯特頻率之上的訊號會發生錯誤
可能需要利用窗函數來補償頻譜洩漏
信號為無限長序列，運算需要截取其中一部分（截斷），於是需要加窗函式，加了窗函式相當於時域相乘，於是相當於頻域卷積，於是頻譜中除了本來該有的主瓣之外，還會出現本不該有的旁瓣，這就是頻譜泄露！為了減弱頻譜泄露，可以採用加權的窗函式，加權的窗函式包括平頂窗、漢寧窗、高斯窗等等。而未加權的矩形窗泄露最為嚴重。

## Slide 19: REFERENCE
https://zh.m.wikipedia.org/zh-tw/T%E6%B3%A2
https://www.edn.com/know-the-limitations-of-your-scopes-fft-capabilities/
https://www.dataq.com/data-acquisition/general-education-tutorials/fft-fast-fourier-transform-waveform-analysis.html

## Slide 20: Thanks for listening!